## Slide 1: DEVELOPMENT OF FUNNEL MODEL FOR ESTIMATION OF LIFE CYCLE GHG EMISSIONS OF VARIOUS TRANSPORTATION FUELS
NSERC/Cenovus/Alberta Innovates Associate Industrial Chair Program in Energy and Environmental Systems Engineering
www.energysystems.ualberta.ca
Webinar
November 19, 2019
Abayomi Oni, Giovanni Di Lullo, Nafisa Mahbub, Amit Kumar
Department of Mechanical Engineering, University of Alberta, Edmonton, Canada

## Slide 2: OVERALL STRUCTURE OF THE NSERC INDUSTRIAL RESEARCH CHAIR PROGRAM

## Slide 3: WEBINAR OUTLINE
Background
The FUNNEL model
Examples of applications
Questions – Please indicate or type your question in the chat box
Sensitivity and uncertainty analysis in FUNNEL-RUST

## Slide 4: CHALLENGES WITH EXISTING MODELS
Models are process specific
  Inaccurate results when plant configuration or feed is modified
  Limited ability to consider future technologies
  Limited to fossil fuels
Models use aggregated or confidential data
  Unable to consider/model alternative or future pathways
  Cannot avoid unnecessary assumptions
  Data not available in public domain
Models do not always consider full life cycle of products
Models are deterministic
  Need to quantify uncertainty
  Sensitivity analysis is generally simplistic

## Slide 5: THE FUNNEL MODEL
What is FUNNEL?
FUNdamental ENgineering PrinciplEs-based ModeL for Estimation of GreenHouse Gases (FUNNEL-GHG)
FUNNEL was developed to accurately evaluate LCA greenhouse gas emission from various energy systems
Developed regression, uncertainty, and sensitivity tool (RUST)

## Slide 6
Liquid
Fossil Fuel
Conventional
Crude Oil
Oil Sands
Future
Technologies
Gaseous
Fossil Fuel
Conventional
Natural Gas
LNG
Renewables
Solar
Energy
Storage
Liquid Biofuel
Transmission
Lines
Pipeline vs.
Rail Transport
OME
HDRD
FUNNEL
NSolve
ESEIEH
THAI
Hydrogen
Wind
With
Storage
Hydro
Power
Pyrolytic
Oil
Algae
Biomass
Biomass / Pellets for
Heat/Electricity

## Slide 7: FUNNEL DATA FLOW
Process Models
ASPEN HYSYS
ASPEN Plus
Custom Solvers
Canada-Wide
Long Range
Energy Planning
(LEAP) Model
Regression, Uncertainty, Sensitivity Tool
(RUST)
FUNNEL
Literature
Correlations
Government Databases
Industry Reports

## Slide 8: INTEGRATING FUNNEL TO PROCESS MODELING TOOLS
Process simulation
Life cycle GHG
estimation in FUNNEL

## Slide 9: INTEGRATING FUNNEL TO PROCESS MODELING TOOLS
  Simulation steps:
  Define the simulation basis
  Characterize feeds
  Install and/or calibrate unit operations
  Run simulation program
  Validate results

## Slide 10: FUNNEL: LCA OF TRANSPORTATION FUELS FROM CONVENTIONAL AND UNCONVENTIONAL CRUDE OIL
Surface Processing
Crude Stabilizer
Gas Dehydrator
Acid Gas Treat.
Water Treat.
Crude Trans.
Pipeline
Ocean Tanker
Refining
Distribution
To Bulk Terminal
  Pipeline
  Rail
  Truck
  Barge
  Ocean Tanker
To Refueling Station via Truck
Extraction
Injection
Lifting
Site Prep.
Well Drilling
Land Use
Fuel
Comb.
Diesel
Electricity,
Natural
Gas
Electricity,
Natural
Gas
Electricity,
Natural
Gas
Electricity,
Diesel
Electricity,
Diesel
Emissions
Emissions
Emissions
Emissions
Emissions
Emissions
Functional Unit: gCO2eq/MJ
Allocation Method: Energy
Emissions

## Slide 11: Demonstrating FUNNEL

## Slide 12: FUNNEL FRAMEWORK
Excel
Interface
User Data
Process Modeling
Output
gCO2eq/MJ
RUST
Sensitivity & Uncertainty Analysis

## Slide 13: INTERFACE OVERVIEW
Color Coding
  Yellow: Required
  Blue: Override recommended
  Purple: Intermediate value
  Green: Output values
User Inputs
Intermediate &
Output Values
Model
Subsection
User Inputs
Intermediate &
Output Values
Model
Subsection

## Slide 14: INTERFACE OVERVIEW: NAVIGATION
Hide Columns
Show/Hide Side-By-Side Scenarios
Jump to Model Subsection
Show/Hide
All Scenarios

## Slide 15: FUNNEL INPUTS EXAMPLE FOR LIQUID FOSSIL FUEL PATHWAYS

## Slide 16: HIGH LEVEL INPUTS
Specify Technology Pathways
Electricity EF can be specified for each stage
  Based on where it is consumed

## Slide 17: FUNNEL DATA INPUT OPTIONS
Multiple calculation options for flexibility

## Slide 18: UPGRADER AND REFINERY INTEGRATION
Currently pulls data from separate Excel book
Input crude oil properties
Calculations use rigorous Aspen Hysys model

## Slide 19: FUNNEL OUTPUT
Output for gasoline results
Similar table for diesel and jet fuel

## Slide 20: Sensitivity and Uncertainty Analysis using RUST

## Slide 21: REGRESSION, UNCERTAINTY, AND SENSITIVITY TOOL (RUST) FOR LCA
Purpose: Streamline LCA process
  Minimize data requirements
Developed for Excel based LCA
  Expanded for use with external models
Includes
  Morris (parameter screening)
  Monte Carlo uncertainty (output uncertainty)
  Sobol contribution to variance (source of uncertainty)
  Multiple parameter linear regression (proxy modeling)

## Slide 22: FUNNEL-RUST: METHODOLOGY FOR LCA
Reduce data collection workload
Three stages
  Screen for key inputs
  Evaluate output uncertainty
  Refine input uncertainty as needed
Morris sensitivity analysis
Determine conservative ranges for all inputs
Parameter sensitivities
Acceptable?
Refine ranges
Probability distributions
Identify key inputs
Perform Monte Carlo
Output distribution
Perform Sobol analysis
Input Sobol indices
Uncertainty range
acceptable?
End
Refine distributions
Yes
No
Yes
No

## Slide 23: FUNNEL-RUST: SENSITIVITY ANALYSIS / SCREENING
 | One-at-a-time (OAT) (Local) | Morris (Global)
Scope | Centered at base case | Explore entire parameter space
Effects | Primary | Primary and interaction
Applicable for | Simple models (linear, aggregated data) | Complex models (non-linear, process/engineering models)
Sampling Method |  | 

## Slide 24: FUNNEL-RUST: MORRIS SCREENING METHOD
Start with conservatively wide ranges
  Simplify data gathering
Majority of parameters are insensitive
Morris Mean:
  r: # of approaches/jumps
Gasoline from Maya Crude (Base Case ~100gCO2eq/MJ)

## Slide 25: FUNNEL-RUST: UNCERTAINTY SOURCES
Empirical / Parameter
  Due to measurement error (flared gas volume), estimating error, variability (SAGD SOR), etc.
Value or Domain (Normative)
  Decided by modeler / stakeholders
  Subjective
  Time horizon, allocation method etc.
Model
  Simplifications
  Error in physical constants
  Extrapolating from similar process

## Slide 26: FUNNEL-RUST: REPRESENTING UNCERTAINTY
Mindset
  Statistical – pure error
  Bayesian – authors confidence
Probabilities
  Convenient single output
  Effects of normative choices is
  unclear
Scenarios
  Clearly shows effect on normative choices
  Large number of outputs
Distrib. | When to use
Uniform | Most conservative
Triangle | Assumed central tendency
PERT | Expected normal distribution
Statistical | Large amount of data

## Slide 27: FUNNEL-RUST: SOBOL CONTRIBUTION OF VARIANCE
What share of output variance does each input contribute?

## Slide 28: FUNNEL-RUST: INTERFACE
Activate UserForm
Model Inputs
Simulation
Inputs
Input Simulation
Parameters

## Slide 29: FUNNEL Example Results

## Slide 30: FUNNEL APPLICATIONS EXAMINED
Three Transportation Fuel LCA:
  Application 1: Conventional and Unconventional Crude Oil
  Application 2: Future Bitumen Extraction Technology
  Application 3: Biofuels, Oxymethylene Ether (OME)

## Slide 31: FUNNEL Application 1: Transportation Fuels from Conventional and Unconventional Crude Oil

## Slide 32: FUNNEL APPLICATION 1 CRUDE & BITUMEN: CURRENT SCENARIOS
Crude | ºAPI | Extraction Technology | Crude Location | Refinery Location
Maya | 22.0 | N2 inj.& gas lift | Mexico | Houston, TX
Mars | 31.5 | Water inj. | U.S. Gulf Coast | Cushing, OK
Bow River | 24.7 | Water inj. & pump lift | Canada | Cushing, OK
Alaska | 31.9 | WAG inj. | Alaska | L.A, CA
Prudhoe Bay | 31.9 | WAG inj. | Alaska | L.A, CA
Kern | 13.0 | Steam inj. & pump lift | California | L.A, CA
Vene | 11.7 | Steam inj. | Venezuela | Houston, TX
Sirri | 31.0 | Water inj. | Iran | Houston, TX
Arab Light | 32.6 | Water inj. | Saudi Arabia | Houston, TX
Bitumen | 8.2 | SAGD & Mining | Alberta | Cushing, OK
SCO | 32.8 | SAGD & Mining | Alberta | Cushing, OK

## Slide 33: FUNNEL APPLICATION 1 CRUDE & BITUMEN: COMPARISON OF FUNNEL TO LITERATURE
Source of Variance
  Different refinery configurations
  VFF emissions are higher in FUNNEL

## Slide 34: FUNNEL APPLICATION 1 CRUDE & BITUMEN: RESULTS
Emissions unlikely correlated to API

## Slide 35: FUNNEL Application 2: Future Bitumen Extraction Technology

## Slide 36: FUNNEL APPLICATION 2 FUTURE TECH.: SCHEMATIC DIAGRAM OF THE ESEIEH PROCESS
Bitumen is separated as dilbit
Solvent (butane) is separated and purified
Heating device
ESEIEH: Enhanced Solvent Extraction Incorporating Electromagnetic Heating technology

## Slide 37: FUNNEL APPLICATION 2 FUTURE TECH.: SCHEMATIC DIAGRAM OF THE ESEIEH PROCESS

## Slide 38: FUNNEL APPLICATION 2 FUTURE TECH.: SCHEMATIC DIAGRAM OF THE ESEIEH PROCESS
Bitumen is separated as dilbit
Solvent (butane) is separated and purified
Heating device
ESEIEH: Enhanced Solvent Extraction Incorporating Electromagnetic Heating technology

## Slide 39: FUNNEL APPLICATION 2 FUTURE TECH.: SCHEMATIC DIAGRAM OF THE ESEIEH PROCESS

## Slide 40: FUNNEL APPLICATION 2 FUTURE TECH.: SCHEMATIC DIAGRAM OF THE ESEIEH PROCESS
Bitumen is separated as dilbit
Solvent (butane) is separated and purified
Heating device
ESEIEH: Enhanced Solvent Extraction Incorporating Electromagnetic Heating technology

## Slide 41: FUNNEL APPLICATION 2 FUTURE TECH.: SCHEMATIC DIAGRAM OF THE ESEIEH PROCESS
Produced
gases

## Slide 42: FUNNEL APPLICATION 2 FUTURE TECHNOLOGY: ESEIEH PATHWAYS
Process simulation was developed for ESEIEH pathways
Aspen HYSYS simulation results were integrated into FUNNEL
Two pathways were considered for ESEIEH process
  In Pathway I, the produced gases are captured to minimize solvent losses, while Pathway II considers their use as fuel
ESEIEH: Enhanced Solvent Extraction Incorporating Electromagnetic Heating Technology

## Slide 43: FUNNEL APPLICATION 2 FUTURE TECHNOLOGY: LIFE CYCLE GHG EMISSION OF THE ESEIEH PROCESS
ESEIEH: Enhanced Solvent Extraction Incorporating Electromagnetic Heating Technology

## Slide 44: FUNNEL APPLICATION 2 FUTURE TECH.: COMPARING ESEIEH WITH NSOLVE
Scenario analysis shows that ESEIEH process can be improved (9.96 kgCO2eq./bbl) by reducing the grid emission intensity
SAGD: 45 – 190 kgCO2 eq./bbl
ESEIEH: Enhanced Solvent Extraction Incorporating Electromagnetic Heating Technology
Solvent Extraction Technology by Nsolve

## Slide 45: FUNNEL Application 3: LCA of Biofuel

## Slide 46: FUNNEL APPLICATION 3 BIOFUEL: OXYMETHYLENE ETHER (OME)
What is oxymethylene ether?
  OME is an oxygenated compound used as a diesel additive in vehicles.
  Can be used in old in-use vehicles; no engine modifications.
  Can reduce soot emissions: 10% OME in 90% diesel reduced soot emissions by 18%
Why oxymethylene ether?
  Unlimited miscibility with diesel
  Properties comparable with diesel: cetane number, flash point, auto ignition point
  Drawbacks of other alternative fuels: DME, biodiesel, methanol

## Slide 47: FUNNEL APPLICATION 3 BIOFUEL: SYSTEM BOUNDARY- OME FROM FOREST BIOMASS

## Slide 48: FUNNEL APPLICATION 3 BIOFUEL: OXYMETHYLENE ETHER PATHWAYS
Oxymethylene ether pathways are:
  Whole Tree
  Forest Residues
Process modelling for oxymethylene ether conversion was developed in Aspen Plus and results integrated into FUNNEL
Information (data and empirical equations) from peer reviewed literature, Alberta specific assumptions, expert inputs and current practices

## Slide 49: FUNNEL APPLICATION 3 BIOFUEL: LIFE CYCLE GHG ASSESSMENT OF OME
WT= Whole Tree; FR= Forest Residue
Life Cycle GHG emissions of Oxymethylene ether from whole tree pathway was 25.99 gCO2eq/MJ whereas forest residue pathway was 17.76 gCO2eq/MJ
10% Oxymethylene ether blended with diesel reduced GHG emissions by 20-21% compared to 100% diesel
10% Oxymethylene ether blended with diesel reduced soot emissions by 30%

## Slide 50: FUNNEL RELATED PUBLICATIONS

## Slide 51: FUNNEL RELATED PUBLICATIONS
Oil Sands
  Nimana, B.; Verma, A.; Di Lullo, G.; Rahman, M.M.; Canter, C.E.; Olateju, B.; Zhang, H.; Kumar, A. Life cycle analysis of bitumen transportation to refineries by rail and pipeline. Environ. Sci. Technol. [Online] 2017, 51, (1), pp 680-691 DOI: http://dx.doi.org/10.1021/acs.est.6b02889.
  Nimana, B.; Canter, C.; Kumar, A. Life cycle assessment of greenhouse gas emissions from Canada's oil sands-derived transportation fuels. Energy [Online] 2015, 88, pp 544-554 DOI: http://dx.doi.org/10.1016/j.energy.2015.05.078.
  Nimana, B.; Canter, C.; Kumar, A. Energy consumption and greenhouse gas emissions in upgrading and refining of Canada's oil sands products. Energy [Online] 2015, 83, pp 65-79 DOI: http://dx.doi.org/10.1016/j.energy.2015.01.085.
  Nimana, B.; Verma, A.; Di Lullo, G.; Rahman, M.M.; Canter, C.E.; Olateju, B.; Zhang, H.; Kumar, A. Life Cycle Analysis of Bitumen Transportation to Refineries by Rail and Pipeline. Environmental Science and Technology [Online] 2017, 51, (1), pp 680-691 DOI: http://doi.org/10.1021/acs.est.6b02889.

## Slide 52: FUNNEL RELATED PUBLICATIONS
Future Oil Sands Technology
  Safaei, M.; Oni, A.O.; Gemechu, E.D.; Kumar, A. Evaluation of energy and greenhouse gas emissions of bitumen-derived transportation fuels from toe-to-heel air injection extraction technology. Fuel [Online] 2019, 256, p 115930 DOI: https://doi.org/10.1016/j.fuel.2019.115930.
  Safaei, M.; Oni, A.O.; Gemechu, E.D.; Kumar, A. Evaluation of energy and GHG emissions’ footprints of bitumen extraction using Enhanced Solvent Extraction Incorporating Electromagnetic Heating technology. Energy [Online] 2019, 186, p 115854 DOI: https://doi.org/10.1016/j.energy.2019.115854.
  Soiket, M.I.H.; Oni, A.O.; Kumar, A. The development of a process simulation model for energy consumption and greenhouse gas emissions of a vapor solvent-based oil sands extraction and recovery process. Energy [Online] 2019, 173, pp 799-808 DOI: https://doi.org/10.1016/j.energy.2019.02.109.
  Soiket, M.I.H.; Oni, A.O.; Gemechu, E.D.; Kumar, A. Life cycle assessment of greenhouse gas emissions of upgrading and refining bitumen from the solvent extraction process. Applied Energy [Online] 2019, 240, pp 236-250 DOI: https://doi.org/10.1016/j.apenergy.2019.02.039.

## Slide 53: FUNNEL RELATED PUBLICATIONS
Conventional Crude Oils
  Rahman, M.M.; Canter, C.; Kumar, A. Well-to-wheel life cycle assessment of transportation fuels derived from different North American conventional crudes. Appl. Energy [Online] 2015, 156, pp 159-173 DOI: http://dx.doi.org/10.1016/j.apenergy.2015.07.004.
  Rahman, M.M.; Canter, C.; Kumar, A. Greenhouse gas emissions from recovery of various North American conventional crudes. Energy [Online] 2014, 74, pp 607-617 DOI: http://dx.doi.org/10.1016/j.energy.2014.07.026.

## Slide 54: FUNNEL RELATED PUBLICATIONS
Uncertainty Analysis
  Di Lullo, G.; Zhang, H.; Kumar, A. Uncertainty in well-to-tank with combustion greenhouse gas emissions of transportation fuels derived from North American crudes. Energy [Online] 2017, 128, pp 475-486 DOI: http://doi.org/10.1016/j.energy.2017.04.040.
  Di Lullo, G.; Zhang, H.; Kumar, A. Evaluation of uncertainty in the well-to-tank and combustion greenhouse gas emissions of various transportation fuels. Appl. Energy [Online] 2016, 184, pp 413-426 DOI: http://doi.org/10.1016/j.apenergy.2016.10.027.
  Di Lullo, G.; Gemechu, E.; Oni, A.O.; Kumar, A. Extending sensitivity analysis using regression to effectively disseminate life cycle assessment results. The International Journal of Life Cycle Assessment [Online] 2019, DOI: http://doi.org/10.1007/s11367-019-01674-y.

## Slide 55: FUNNEL RELATED PUBLICATIONS
Natural Gas
  Raj, R.; Ghandehariun, S.; Kumar, A.; Linwei, M. A well-to-wire life cycle assessment of Canadian shale gas for electricity generation in China. Energy [Online] 2016, 111, pp 642-652 DOI: https://doi.org/10.1016/j.energy.2016.05.079.
  Sapkota, K.; Oni, A.O.; Kumar, A. Techno-economic and life cycle assessments of the natural gas supply chain from production sites in Canada to north and southwest Europe. J. Nat. Gas Sci. Eng. [Online] 2018, DOI: https://doi.org/10.1016/j.jngse.2018.01.048.

## Slide 56: FUNNEL RELATED PUBLICATIONS
Biofuel
  Mahbub, N.; Gemechu, E.; Zhang, H.; Kumar, A. The life cycle greenhouse gas emission benefits from alternative uses of biofuel coproducts. Sustainable Energy Technologies and Assessments [Online] 2019, 34, pp 173-186 DOI: https://doi.org/10.1016/j.seta.2019.05.001.
  Mahbub, N.; Oyedun, A.O.; Zhang, H.; Kumar, A.; Poganietz, W.-R. A life cycle sustainability assessment (LCSA) of oxymethylene ether as a diesel additive produced from forest biomass. The International Journal of Life Cycle Assessment [Online] 2019, 24, (5), pp 881-899 DOI: 10.1007/s11367-018-1529-6.
  Mahbub, N.; Oyedun, A.O.; Kumar, A.; Oestreich, D.; Arnold, U.; Sauer, J. A life cycle assessment of oxymethylene ether synthesis from biomass-derived syngas as a diesel additive. Journal of Cleaner Production [Online] 2017, 165, pp 1249-1262 DOI: 10.1016/j.jclepro.2017.07.178.
  Miller, P.; Kumar, A. Development of emission parameters and net energy ratio for renewable diesel from Canola and Camelina. Energy [Online] 2013, 58, pp 426-437.
  Wong, A.; Zhang, H.; Kumar, A. Life cycle assessment of renewable diesel production from lignocellulosic biomass. The International Journal of Life Cycle Assessment [Online] 2016, 21, (10), pp 1404-1424.
  Oyedun, A.O.; Patel, M.; Kumar, M.; Kumar, A. Upgrading of bio-oil via hydrodeoxygenation. In Chemical Catalysts for Biomass Upgrading; Brown, R., Ed. Wiley-VCH: in press.

## Slide 57: FUNNEL RELATED PUBLICATIONS
Hydrogen
  Ghandehariun, S.; Kumar, A. Life cycle assessment of wind-based hydrogen production in Western Canada. International Journal of Hydrogen Energy [Online] 2016, 41, (22), pp 9696-9704 DOI: https://doi.org/10.1016/j.ijhydene.2016.04.077.
  Olateju, B.; Monds, J.; Kumar, A. Large scale hydrogen production from wind energy for the upgrading of bitumen from oil sands. Applied Energy [Online] 2014, 118, pp 48-56 DOI: https://doi.org/10.1016/j.apenergy.2013.12.013.
  Sarkar, S.; Kumar, A. Large-scale biohydrogen production from bio-oil. Bioresource technology [Online] 2010, 101, (19), pp 7350-7361.
  Kumar, M.; Oni, A.O.; Kumar, A. Biohydrogen production from bio-oil via hydrothermal liquefaction. In Biofuels; Elsevier Inc.: Amsterdam, The Netherlands, in press.
  Kumar, M.; Oyedun, A.O.; Kumar, A. A comparative analysis of hydrogen production from the thermochemical conversion of algal biomass. International Journal of Hydrogen Energy [Online] 2019, 44, (21), pp 10384-10397 DOI: https://doi.org/10.1016/j.ijhydene.2019.02.220.

## Slide 58: FUNNEL RELATED PUBLICATIONS
Storage
  Thaker, S.; Oni, A.O.; Gemechu, E.; Kumar, A. Evaluating energy and greenhouse gas emission footprints of thermal energy storage systems for concentrated solar power applications. Journal of Energy Storage [Online] 2019, 26, p 100992 DOI: https://doi.org/10.1016/j.est.2019.100992.
  Kapila, S.; Oni, A.O.; Gemechu, E.D.; Kumar, A. Development of net energy ratios and life cycle greenhouse gas emissions of large-scale mechanical energy storage systems. Energy [Online] 2019, 170, pp 592-603 DOI: https://doi.org/10.1016/j.energy.2018.12.183.

## Slide 59: FUNNEL RELATED PUBLICATIONS
Biomass / Pellets for Heat / Electricity
  Thakur, A.; Canter, C.E.; Kumar, A. Life-cycle energy and emission analysis of power generation from forest biomass. Applied Energy [Online] 2014, 128, pp 246-253.
  Kabir, M.R.; Kumar, A. Comparison of the energy and environmental performances of nine biomass/coal co-firing pathways. Bioresource technology [Online] 2012, 124, pp 394-405.
  Sultana, A.; Kumar, A. Development of energy and emission parameters for densified form of lignocellulosic biomass. Energy [Online] 2011, 36, (5), pp 2716-2732.
  Shahrukh, H.; Oyedun, A.O.; Kumar, A.; Ghiasi, B.; Kumar, L.; Sokhansanj, S. Net energy ratio for the production of steam pretreated biomass-based pellets. Biomass and Bioenergy [Online] 2015, 80, (0), pp 286-297 DOI: http://dx.doi.org/10.1016/j.biombioe.2015.06.006.
  Shahrukh, H.; Oyedun, A.O.; Kumar, A.; Ghiasi, B.; Kumar, L.; Sokhansanj, S. Comparative net energy ratio analysis of pellet produced from steam pretreated biomass from agricultural residues and energy crops. Biomass and Bioenergy [Online] 2016, 90, pp 50-59 DOI: doi:10.1016/j.biombioe.2016.03.022.
Other Publications and Presentations
  http://www.ualbertaenergysystems.ca/

## Slide 60: ACKNOWLEDGMENTS
Thanks to the NSERC/Cenovus/Alberta Innovates Associate Industrial Research Chair in Energy and Environmental Systems Engineering and the Cenovus Energy Endowed Chair in Environmental Engineering for providing financial support.
We are also grateful to representatives from Cenovus Energy Inc., Alberta Innovates, Suncor Energy Inc., Environment and Climate Change Canada, Natural Resources Canada, and Alberta Department of Energy for their valuable inputs and comments in various forms.
As a part of the University of Alberta's Future Energy Systems (FES) research initiative, this research was made possible in part thanks to funding from the Canada First Research Excellence Fund (CFREF).

## Slide 61: THANK YOU / QUESTIONS
  For further information:
Website: www.energysystem.ualberta.ca
Amit Kumar, Prof. NSERC/Cenovus/Alberta Innovates Associate Industrial Research Chair in Energy and Environmental Systems Engineering
Cenovus Energy Endowed Chair in Environmental Engineering
Deputy Director: Future Energy Systems
Department of mechanical engineering, University of Alberta. E-mail: Amit.Kumar@ualberta.ca