## Slide 1: Integrated Assessment of Environmental Footprints of Energy Pathways
NSERC/Cenovus/Alberta Innovates Associate Industrial Chair Program in Energy and Environmental Systems Engineering
www.energysystems.ualberta.ca
Webinar
March 3, 2020
Thomas Patrick, Matthew Davis, Eskinder Gemechu, Amit Kumar
Department of Mechanical Engineering, University of Alberta, Edmonton, Canada

## Slide 2: Overall Structure of the NSERC Industrial Research Chair Program

## Slide 3: LEAP/WEAP GROUP
Group members:
  Eskinder Gemechu, PDF
  Matthew Davis, Research Engineer
  Saeidreza Radpour, PhD student
  Christophe Owttrim, MSc student
  Thomas Patrick, MSc student
  Minza Haider, MSc student
  Ayodeji Okunlola, PhD student
Past HQPs: 18
  PDF: 2
  PhD: 2
  MSc: 10
  RA/Undergrads/Interns: 4

## Slide 4: OUTLINE
Modelling approach
The WEAP-Canada model
Summary of research on integrated assessments
Questions – Please type your question in the chat box or just indicate that you have a question to ask
Long-range Energy Alternative Planning (LEAP) Model integration with WEAP
Water Evaluation and Planning (WEAP) Model
Life cycle water footprints

## Slide 5: GENERALIZED MODELLING APPROACH
Process Modelling
Environmental Assessment/
Cost Estimation
Energy/Water Modelling
Outputs
Technology characterization
e.g. Renewable-based power generation
Specification of unit operations for each alternative pathways
Characterization process equipment for unit operations
Determination of energy/resource inputs for each process equipment
Environmental Modelling
(Life Cycle Assessment)
g CO2 eq per unit output
m3 water per unit output
Economic Modelling
(Techno-Economic Assessment)
Cost metrics
$ per unit output
Water modelling
(WEAP - Water Evaluation And Planning)
Canada-wide
Water demand
Water supply
Energy modelling
(LEAP - Long-range Energy Alternatives Planning)
Canada-wide
Energy demand
Energy supply
Long-term annual results per scenario
Total water withdrawal
Total water consumption
Total water savings
Long-term annual results per scenario
Energy demand
Technology use
GHG emissions
System costs
$/tonne of CO2 abatement
$/liter of water saved

## Slide 6: GENERALIZED MODELLING APPROACH
Process Modelling
Environmental Assessment/
Cost Estimation
Energy/Water Modelling
Outputs
Technology characterization
e.g. Renewable-based power generation
Specification of unit operations for each alternative pathways
Characterization process equipment for unit operations
Determination of energy/resource inputs for each process equipment
Environmental Modelling
(Life Cycle Assessment)
g CO2 eq per unit output
m3 water per unit output
Economic Modelling
(Techno-Economic Assessment)
Cost metrics
$ per unit output
Water modelling
(WEAP - Water Evaluation And Planning)
Canada-wide
Water demand
Water supply
Energy modelling
(LEAP - Long-range Energy Alternatives Planning)
Canada-wide
Energy demand
Energy supply
Long-term annual results per scenario
Total water withdrawal
Total water consumption
Total water savings
Long-term annual results per scenario
Energy demand
Technology use
GHG emissions
System costs
$/tonne of CO2 abatement
$/liter of water saved

## Slide 7: LIFE CYCLE WATER FOOTPRINTS

## Slide 8: LIFE CYCLE ASSESSMENT – WATER FOOTPRINTS
System approach and based on life cycle thinking
Source: Life Cycle Initiative (http://www.lifecycleinitiative.org)
Goal and Scope Definition
Life Cycle Inventory Analysis
Life Cycle Impact Assessment
Interpretation
Life cycle assessment framework according to ISO

## Slide 9: WATER-DEMAND COEFFICIENT – DEFINITIONS
Water footprint: The total volume of freshwater used in the life cycle of a product system – L/kWh, L/tonne, L/bbl
Water withdrawal: The total volume of water removed from a water source
Water consumed: The amount of water removed for use but not returned to its source (includes evaporation, transpiration and direct consumption)
Water returned: The amount of water sent back to the source (effluent)

## Slide 10: WATER-DEMAND COEFFICIENT FRAMEWORK
Coal-based power generation technologies
Gas-fired power generation technologies
Power generation from renewable energy technologies
Crude oil production
Oil sands-based transportation fuel
Others

## Slide 11: WATER FOOTPRINTS FOR CRUDE OIL PRODUCTION, UPGRADING, AND REFINING
Water footprint for 4 major pathways were developed
Ali and Kumar (2017), Energy, vol. 131, pp. 41-49, 2017.

## Slide 12: WATER FOOTPRINTS FOR RENEWABLE POWER GENERATION TECHNOLOGIES
Water footprint for 60 renewable energy based power generation pathways were developed
Ali and Kumar (2017), Energy Conversion and Management, vol. 143, pp. 470-481, 2017.

## Slide 13: WATER FOOTPRINTS FOR GAS-FIRED POWER GENERATION TECHNOLOGIES
Gas sources
Gas processes
Gas delivery
Power plant technology
Cooling system
Conventional gas
Coal-bed methane (CBM)
Shale gas
Exploration
Drilling
Pipeline
Storage
Distribution
Single cycle
Combined cycle (NGCC)
Steam cycle
Cogeneration
Once-through cooling
Cooling tower
Cooling pond
Dry cooling
Water-demand coefficients were developed for 18 generic pathways
Fracturing
Water produced
Well abandonment
Other
Ali and Kumar (2016), Energy Conversion and Management, vol. 110, pp. 386-396.

## Slide 14: WATER FOOTPRINTS FOR COAL-BASED POWER GENERATION TECHNOLOGIES
Coal mining
Coal preparation
Coal transportation
Power plant technology
Cooling system
Other operation
Surface mining without revegetation
Surface mining with revegetation
Underground mining
Crushing
Washing
Truck
Rail
Barge
Conveyor
Slurry pipeline
Coal log pipeline
Subcritical
Supercritical
Ultra-supercritical
Integrated combined cycle (IGCC)
Once-through cooling
Cooling tower
Cooling pond
Dry cooling
Ash handling
Drinking
Dust suppression
Desulphurization
Plant decommissioning
Water-demand coefficients for 36 different electricity generation pathways
Ali and Kumar (2015), Energy Conversion and Management, vol. 90, pp. 247-260

## Slide 15: GENERALIZED MODELLING APPROACH
Process Modelling
Environmental Assessment/
Cost Estimation
Energy/Water Modelling
Outputs
Technology characterization
e.g. Renewable-based power generation
Specification of unit operations for each alternative pathways
Characterization process equipment for unit operations
Determination of energy/resource inputs for each process equipment
Environmental Modelling
(Life Cycle Assessment)
g CO2 eq per unit output
m3 water per unit output
Economic Modelling
(Techno-Economic Assessment)
Cost metrics
$ per unit output
Water modelling
(WEAP - Water Evaluation And Planning)
Canada-wide
Water demand
Water supply
Energy modelling
(LEAP - Long-range Energy Alternatives Planning)
Canada-wide
Energy demand
Energy supply
Long-term annual results per scenario
Total water withdrawal
Total water consumption
Total water savings
Long-term annual results per scenario
Energy demand
Technology use
GHG emissions
System costs
$/tonne of CO2 abatement
$/liter of water saved

## Slide 16: WATER EVALUATION AND PLANNING (WEAP)

## Slide 17: BACKGROUND & WEAP CHARACTERISTICS
Background
  A modelling framework is required to implement our understanding of a complex system
  WEAP is developed by the Stockholm Environmental Institute, with support from US Army Corps of Engineers, the World Bank, and many others
  Used by a variety of academic and other groups internationally, such as the UN Department of Economic and Social Affairs
Key characteristics of WEAP
  Simple to understand and use
  Wide ranging features available but optional
  Built in compatibility with Long-range Energy Alternatives Planning (LEAP) model for energy modelling

## Slide 18: WEAP FRAMEWORK

## Slide 19: WEAP-CANADA MAIN ELEMENTS
Sample model creation:
Water use of bitumen mining

## Slide 20: WEAP-CANADA MAIN ELEMENTS (OIL AND GAS SECTOR)
Graphical user interface (GUI)
Geographical information system (GIS)
Water supply sources
Water demand sites
Demand site activity
Water-use intensities
Optimization
Scenario analysis
WEAP

## Slide 22: WEAP-CANADA MAIN ELEMENTS (OIL AND GAS SECTOR)
Graphical user interface (GUI)
Geographical information system (GIS)
Water supply sources
Water demand sites
Demand site activity
Water-use intensities
Optimization
Scenario analysis
WEAP

## Slide 23
Athabasca River not included in base
model geography

## Slide 24
Vector layer added showing
Canada’s water features

## Slide 25: WEAP-CANADA MAIN ELEMENTS (OIL AND GAS SECTOR)
Graphical user interface (GUI)
Geographical information system (GIS)
Water supply sources
Water demand sites
Demand site activity
Water-use intensities
Optimization
Scenario analysis
WEAP

## Slide 27
The light blue line
is the river feature

## Slide 28
The light blue line
is the river feature

## Slide 29
Headflow (monthly)
Dec
2015
Jan
2015
Scenario selected: Current Accounts (2015)
Item selected: Athabasca River
Panel on right: shows data for this river

## Slide 30
Scenario selected: Reference (2016-2050)
Headflow (monthly)
Dec
2050
Jan
2015
Item selected: Athabasca River
Panel on right: shows data for this river

## Slide 31: WEAP-CANADA MAIN ELEMENTS (OIL AND GAS SECTOR)
Graphical user interface (GUI)
Geographical information system (GIS)
Water supply sources
Water demand sites
Demand site activity
Water-use intensities
Optimization
Scenario analysis
WEAP

## Slide 34: WEAP-CANADA MAIN ELEMENTS (OIL AND GAS SECTOR)
Graphical user interface (GUI)
Geographical information system (GIS)
Water supply sources
Water demand sites
Demand site activity
Water-use intensities
Optimization
Scenario analysis
WEAP

## Slide 35
Item selected:
Total bitumen mined
Scenario selected: Current Accounts (2015)
Input value: 184.65 thousand m3/d
(historic data)

## Slide 36
CER mined bitumen projection to 2040,
then extrapolated to 2050
2015: ~185 thousand m3/d (1.16 Mb/d)
2050: ~260 thousand m3/d (1.65 Mb/d)
Scenario selected: Reference (2016-2050)
Item selected:
Total bitumen mined

## Slide 37: WEAP-CANADA MAIN ELEMENTS (OIL AND GAS SECTOR)
Graphical user interface (GUI)
Geographical information system (GIS)
Water supply sources
Water demand sites
Demand site activity
Water-use intensities
Optimization
Scenario analysis
WEAP

## Slide 38
Footprint: 2.41 m3 water/m3 bitumen
From AER water use report
Consumption: 82%
From literature
New quantities defined for:
Bitumen mining footprint
Bitumen mining consumption

## Slide 39: WEAP-CANADA MAIN ELEMENTS (OIL AND GAS SECTOR)
Graphical user interface (GUI)
Geographical information system (GIS)
Water supply sources
Water demand sites
Demand site activity
Water-use intensities
Optimization
Scenario analysis
WEAP

## Slide 40: WEAP-CANADA MAIN ELEMENTS - OPTIMIZATION
WEAP calculates water behaviour with a linear program
  Optimizes demand site coverage and any instream flow requirements
  Contingent on demand priorities, supply preferences, etc.
Optimization of cost / technology choices done in LEAP

## Slide 41
Model parameters:
This model contains one demand site: bitumen mining
Activity level: CER projection
Water footprint: assumes 2015 value over entire model duration

## Slide 42: WEAP-CANADA MAIN ELEMENTS (OIL AND GAS SECTOR)
Graphical user interface (GUI)
Geographical information system (GIS)
Water supply sources
Water demand sites
Demand site activity
Water-use intensities
Optimization
Scenario analysis
WEAP

## Slide 43
High and low price scenarios will be based on CER high and low
price projections for volume of bitumen production

## Slide 44: WEAP-CANADA OIL AND GAS PRICE SCENARIOS
CER oil production forecast based on long term oil price
Reference scenario forecast: ≈$60/barrel WCS
Low price: ≈$20/barrel WCS
High price: ≈$100/barrel WCS
Chart: Mined Bitumen - CER Projection
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Low price | 0.62648 | 0.76046 | 0.78436 | 0.72146 | 0.82525 | 0.85695 | 0.89255 | 0.9323 | 0.97608 | 0.96017 | 1.1614 | 1.15 | 1.2757 | 1.4769 | 1.5889 | 1.6053 | 1.6053 | 1.6053 | 1.6053 | 1.6053 | 1.6053 | 1.6024 | 1.5971 | 1.5918 | 1.5866 | 1.5814 | 1.5731 | 1.5622 | 1.5515 | 1.5408 | 1.5303 | 1.5199 | 1.5097 | 1.4995 | 1.4895 | 1.4796 | 1.4695 | 1.4593 | 1.4492 | 1.4391 | 1.4289 | 1.4188 | 1.4086 | 1.3985 | 1.3884 | 1.3782
Reference | 0.62648 | 0.76046 | 0.78436 | 0.72146 | 0.82525 | 0.85695 | 0.89255 | 0.9323 | 0.97608 | 0.96017 | 1.1614 | 1.15 | 1.2757 | 1.4769 | 1.5987 | 1.633 | 1.6418 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469
High Price | 0.62648 | 0.76046 | 0.78436 | 0.72146 | 0.82525 | 0.85695 | 0.89255 | 0.9323 | 0.97608 | 0.96017 | 1.1614 | 1.15 | 1.2757 | 1.4769 | 1.6071 | 1.6615 | 1.6716 | 1.7028 | 1.747 | 1.7557 | 1.7725 | 1.8054 | 1.8305 | 1.8306 | 1.8306 | 1.8644 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847

## Slide 45
High price scenario
Reference scenario
Low price scenario
Total water demand in model

## Slide 46: WEAP-CANADA OIL AND GAS
Actual model

## Slide 47: WEAP-CANADA OIL AND GAS
Subsectors included in model
  Conventional oil
  Natural gas – well creation
  Bitumen – surface mines
  Bitumen – in situ
  Upgrading
  Refining

## Slide 48: WEAP-CANADA OIL AND GAS FRAMEWORK
River basin
Sub-sector (demand node)
River basin “A”
Technology/site distinctions
Bitumen mining
Bitumen TIS
Conventional oil
Natural gas
Refining
Upgrading
Mine 1 Mine 2 [...]
CSS SADG Primary
Drilling Fracturing

## Slide 49: WEAP-CANADA OIL AND GAS SCHEMATIC
6 subsectors
38 demand sites
19 river basins
Covers all provinces
2005-2050

## Slide 50
Alberta: many o&g sites, all subsectors
Manitoba: some conventional oil
Atlantic: refining, offshore oil
Eastern Canada: mostly refining, some oil
Saskatchewan: oil, natural gas, refining
WEAP-Canada Oil and Gas demand sites
6 subsectors
38 demand sites
19 river basins
Covers all provinces
2005-2050
BC: natural gas, oil, and refining

## Slide 51
Withdrawal intensity by mining site
CNRL Horizon
Albian Sands
Suncor Fort Hills
Imperial Oil Kearl
Suncor Base
Syncrude Base
Production share (% of total) by site
Key assumptions for bitumen mining

## Slide 52
Albian Sands
Suncor base
Syncrude base
In base year (2005)
only three mines are
operating (Suncor,
Syncrude, and Albian
Sands)
Activity by mining site
CNRL Horizon
Albian Sands
Suncor Fort Hills
Imperial Oil Kearl
Suncor Base
Syncrude Base

## Slide 53
Conventional oil demand node
subdivided by river basin
Oldman: <1%
Bow: 26%
South Saskatchewan: 17%
North Saskatchewan: 39%
Peace: 18%
Key assumptions for conventional oil subsector
Withdrawal intensity (2005): 0.613 m3 water / m3 oil
(calculated from CAPP data)
Consumption: 92% (literature)
Production volume: CER data

## Slide 54
Key assumptions for natural gas subsector
Subsector has two technologies, drilling and fracturing
Activity and footprint data needed for each
Drilling data
Withdrawal intensity: 500 m3/well
(CAPP data)
Consumption: 100% (inferred)
Drilling activity: CER data
Fracturing data
Withdrawal intensity: 12,000-53,000 m3/well
(Calculated with AER and CER data)
Consumption: 100% (inferred)
Fracturing activity: CER data

## Slide 55: WEAP-CANADA OIL AND GAS
Preliminary results and scenarios

## Slide 56: WEAP-CANADA OIL AND GAS RESULTS
Chart: Oil and gas water consumption by province
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
BC | 20.7539 | 19.3754 | 15.4664 | 13.0388 | 6.2428 | 7.3209 | 4.2107 | 2.5819 | 2.9472 | 4.2159 | 4.1429 | 5.0659 | 9.1784 | 11.2339 | 12.6634 | 12.7831 | 13.2069 | 13.5918 | 13.712 | 14.1027 | 15.217 | 15.7819 | 14.2112 | 14.1056 | 13.8848 | 15.9878 | 16.7322 | 16.3295 | 16.6879 | 17.0721 | 17.3378 | 17.705 | 17.8892 | 18.3789 | 18.8376 | 19.2864 | 19.6835 | 20.0637 | 20.4608 | 20.841 | 21.238 | 21.6113 | 22.0154 | 22.4054 | 22.7926 | 23.1828
AB | 194.5767 | 213.4444 | 212.2398 | 194.0024 | 192.0547 | 203.7932 | 193.3806 | 202.6361 | 213.8932 | 199.0535 | 228.3561 | 217.3567 | 251.3732 | 284.9107 | 299.9534 | 306.4885 | 309.6907 | 311.6395 | 314.0018 | 316.7796 | 310.3917 | 312.4512 | 313.3613 | 314.3351 | 316.0581 | 320.0046 | 323.8873 | 326.5469 | 329.1348 | 330.8366 | 332.73 | 334.2222 | 335.6526 | 337.2875 | 338.7665 | 340.2058 | 341.728 | 343.2166 | 344.7512 | 346.2472 | 347.7864 | 349.2925 | 350.8427 | 352.5826 | 354.3321 | 356.127
SK | 19.8614 | 20.3539 | 20.9184 | 19.2031 | 20.4848 | 19.5926 | 19.9937 | 20.3184 | 19.3277 | 17.538 | 18.1377 | 18.4602 | 19.6204 | 19.8672 | 20.3789 | 21.8804 | 21.9561 | 22.0905 | 22.1546 | 22.3456 | 23.7743 | 23.7758 | 23.7758 | 23.8379 | 24.0001 | 25.3957 | 25.3967 | 25.3967 | 25.3967 | 25.3967 | 25.3967 | 25.3967 | 25.3967 | 25.3967 | 25.3967 | 25.3967 | 25.3967 | 25.3967 | 25.3967 | 25.3967 | 25.3967 | 25.3967 | 25.3967 | 25.3967 | 25.3967 | 25.3967
MT | 0.2826 | 0.25214 | 0.19541 | 0.25739 | 0.23953 | 0.39502 | 0.39292 | 0.30887 | 0.41393 | 0.58307 | 0.48011 | 1.0198 | 1.1148 | 1.3816 | 1.5101 | 1.478 | 1.501 | 1.6433 | 1.7672 | 2.0472 | 2.5475 | 2.8642 | 2.0518 | 2.038 | 2.0151 | 3.0111 | 3.0891 | 2.5337 | 2.4465 | 2.4878 | 2.4511 | 2.4924 | 2.4465 | 2.5016 | 2.5475 | 2.598 | 2.6255 | 2.6531 | 2.6806 | 2.7082 | 2.7357 | 2.7587 | 2.7908 | 2.8137 | 2.8459 | 2.8688
ON | 17.097 | 14.8729 | 14.2969 | 14.6518 | 6.103 | 4.4485 | 3.9785 | 3.7317 | 3.2953 | 2.6901 | 2.8449 | 2.742 | 4.4949 | 4.8313 | 4.9251 | 4.8313 | 4.7375 | 4.6437 | 4.9641 | 4.9172 | 4.9641 | 4.9641 | 4.9172 | 5.2377 | 5.2377 | 5.2846 | 5.3784 | 5.4253 | 5.5191 | 5.566 | 5.6129 | 5.6598 | 5.7072 | 5.7541 | 5.801 | 5.8479 | 5.8939 | 5.9408 | 5.9877 | 6.0346 | 6.0815 | 6.1284 | 6.1753 | 6.2222 | 6.2691 | 6.316
QC | 0.65662 | 0.64154 | 0.65188 | 0.58824 | 0.6194 | 0.57657 | 0.55339 | 0.56662 | 0.50934 | 0.41564 | 0.43986 | 0.42415 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939 | 0.42939
Atlantic | 2.8539 | 2.5565 | 1.9179 | 2.4672 | 2.2069 | 3.5781 | 3.5356 | 2.78 | 3.7221 | 5.2398 | 4.311 | 9.1549 | 10.0094 | 12.4041 | 13.5582 | 13.2698 | 13.4758 | 14.7532 | 15.8657 | 18.3793 | 22.8707 | 25.7139 | 18.4205 | 18.2969 | 18.0908 | 27.0324 | 27.7329 | 22.7471 | 21.9642 | 22.3354 | 22.0058 | 22.3766 | 21.9646 | 22.4591 | 22.8711 | 23.3244 | 23.5715 | 23.8187 | 24.066 | 24.3132 | 24.5604 | 24.7665 | 25.0549 | 25.2609 | 25.5494 | 25.7554
Territories | 1.5843 | 1.3243 | 1.2519 | 1.3458 | 0.26138 | 0.089806 | 0.049594 | 0.0080423 | 0 | 0 | 0 | 0 | 0.21469 | 0.21669 | 0.2284 | 0.21669 | 0.20497 | 0.19326 | 0.19326 | 0.1874 | 0.19326 | 0.19326 | 0.1874 | 0.1874 | 0.1874 | 0.19326 | 0.20497 | 0.21083 | 0.22254 | 0.2284 | 0.23425 | 0.24011 | 0.24597 | 0.25182 | 0.25768 | 0.26354 | 0.26939 | 0.27525 | 0.2811 | 0.28696 | 0.29282 | 0.29867 | 0.30453 | 0.31039 | 0.31624 | 0.3221
CER reference projections for activity levels
No assumed footprint (water intensity) improvements

## Slide 57: WEAP-CANADA OIL AND GAS RESULTS
Chart: Oil and gas water consumption by subsector
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
NGext | 82.2634 | 75.1124 | 61.5559 | 55.129 | 23.6637 | 26.528 | 16.352 | 10.2662 | 12.048 | 17.1596 | 16.1976 | 22.7132 | 38.1403 | 46.3742 | 51.8126 | 51.8633 | 53.2363 | 55.294 | 56.5066 | 59.5653 | 66.4783 | 70.3822 | 59.9353 | 59.5125 | 58.6679 | 72.0174 | 74.975 | 70.0181 | 70.6537 | 72.1858 | 72.8204 | 74.2992 | 74.6175 | 76.5718 | 78.3674 | 80.1631 | 81.6413 | 83.0672 | 84.5464 | 85.9729 | 87.4515 | 88.8252 | 90.3572 | 91.7831 | 93.2623 | 94.6887
Bmining | 99.2839 | 120.5163 | 124.3042 | 114.3359 | 129.4165 | 137.477 | 139.1359 | 146.4483 | 156.5706 | 137.7475 | 168.2729 | 157.0254 | 177.6459 | 205.6565 | 213.4977 | 218.0842 | 219.2602 | 219.9406 | 219.9406 | 219.9406 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185 | 210.3185
Binsitu | 6.9207 | 7.9888 | 9.1675 | 10.4672 | 12.4328 | 13.896 | 15.4938 | 18.9709 | 21.08 | 24.9898 | 27.2188 | 28.8414 | 33.3619 | 34.5206 | 38.2034 | 39.7675 | 40.5008 | 41.1872 | 43.1402 | 45.6957 | 47.9555 | 49.8489 | 51.3989 | 52.3264 | 54.0657 | 56.4478 | 58.859 | 60.5328 | 61.8216 | 62.438 | 63.1554 | 63.6469 | 64.2471 | 64.8242 | 65.2814 | 65.7425 | 66.2712 | 66.8038 | 67.3423 | 67.882 | 68.4293 | 68.9765 | 69.5319 | 70.0895 | 70.6499 | 71.2161
ConvOil | 44.437 | 44.0621 | 46.1278 | 42.0294 | 37.5924 | 37.9984 | 30.9897 | 32.6992 | 31.2813 | 29.1993 | 25.6032 | 24.0182 | 24.4622 | 25.3316 | 26.2296 | 26.2571 | 26.7241 | 26.9475 | 27.5008 | 27.7959 | 28.0161 | 28.0031 | 28.0809 | 28.307 | 28.6854 | 28.9938 | 29.1361 | 29.1876 | 29.4449 | 29.8477 | 30.3412 | 30.6953 | 30.9867 | 31.1822 | 31.3777 | 31.5656 | 31.8045 | 32.0422 | 32.2838 | 32.5215 | 32.7592 | 32.9994 | 33.2397 | 33.6679 | 34.1383 | 34.6125
Upgrader | 6.7093 | 7.504 | 7.8612 | 7.4207 | 8.0783 | 8.044 | 8.9095 | 8.969 | 9.1258 | 9.2128 | 9.3274 | 9.9645 | 11.0198 | 11.2666 | 11.7783 | 13.2799 | 13.3555 | 13.49 | 13.554 | 13.745 | 15.1737 | 15.1752 | 15.1752 | 15.2374 | 15.3996 | 16.7951 | 16.7961 | 16.7961 | 16.7961 | 16.7961 | 16.7961 | 16.7961 | 16.7961 | 16.7961 | 16.7961 | 16.7961 | 16.7961 | 16.7961 | 16.7961 | 16.7961 | 16.7961 | 16.7961 | 16.7961 | 16.7961 | 16.7961 | 16.7961
Refining | 18.0522 | 17.6375 | 17.9219 | 16.1723 | 17.0289 | 15.8513 | 15.214 | 15.5779 | 14.003 | 11.427 | 12.0929 | 11.661 | 11.805 | 12.1254 | 12.1254 | 12.1254 | 12.1254 | 12.1254 | 12.4458 | 12.4458 | 12.4458 | 12.4458 | 12.4458 | 12.7663 | 12.7663 | 12.7663 | 12.7663 | 12.7663 | 12.7663 | 12.7663 | 12.7663 | 12.7663 | 12.7663 | 12.7663 | 12.7663 | 12.7663 | 12.7663 | 12.7663 | 12.7663 | 12.7663 | 12.7663 | 12.7663 | 12.7663 | 12.7663 | 12.7663 | 12.7663
CER reference projections for activity levels
No assumed footprint (water intensity) improvements

## Slide 58: WEAP-CANADA OIL AND GAS SCENARIO BACKGROUND
Chart: Low Price ($20/bbl)
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Mined bitumen | 1.4769 | 1.5889 | 1.6053 | 1.6053 | 1.6053 | 1.6053 | 1.6053 | 1.6053 | 1.6024 | 1.5971 | 1.5918 | 1.5866 | 1.5814 | 1.5731 | 1.5622 | 1.5515 | 1.5408 | 1.5303 | 1.5199 | 1.5097 | 1.4995 | 1.4895 | 1.4796 | 1.4695 | 1.4593 | 1.4492 | 1.4391 | 1.4289 | 1.4188 | 1.4086 | 1.3985 | 1.3884 | 1.3782
In situ bitumen | 1.6457 | 1.6744 | 1.7132 | 1.7479 | 1.7444 | 1.7407 | 1.7357 | 1.7265 | 1.7157 | 1.7057 | 1.6962 | 1.6873 | 1.6688 | 1.6431 | 1.6185 | 1.5948 | 1.5719 | 1.5348 | 1.4878 | 1.4435 | 1.3935 | 1.3395 | 1.2888 | 1.2395 | 1.1903 | 1.141 | 1.0917 | 1.0424 | 0.99311 | 0.94383 | 0.89454 | 0.84526 | 0.79597
Conventional oil | 1.2525 | 1.2517 | 1.1948 | 1.1752 | 1.1241 | 1.1172 | 1.0861 | 1.0464 | 0.96721 | 0.9206 | 0.87381 | 0.83607 | 0.79197 | 0.75191 | 0.69857 | 0.67102 | 0.6463 | 0.6256 | 0.60353 | 0.58686 | 0.56755 | 0.55 | 0.53226 | 0.51379 | 0.49531 | 0.47684 | 0.45836 | 0.43989 | 0.42141 | 0.40294 | 0.38446 | 0.36599 | 0.34751
Chart: Reference Price ($60/bbl)
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Mined bitumen | 1.4769 | 1.5987 | 1.633 | 1.6418 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469 | 1.6469
In situ bitumen | 1.6457 | 1.722 | 1.7843 | 1.8136 | 1.841 | 1.9189 | 2.0208 | 2.111 | 2.1865 | 2.2483 | 2.2853 | 2.3547 | 2.4497 | 2.5459 | 2.6127 | 2.6641 | 2.6887 | 2.7173 | 2.7369 | 2.7608 | 2.7838 | 2.8021 | 2.8205 | 2.8415 | 2.8625 | 2.8835 | 2.9045 | 2.9254 | 2.9464 | 2.9674 | 2.9884 | 3.0094 | 3.0304
Conventional oil | 1.2526 | 1.2968 | 1.2981 | 1.321 | 1.332 | 1.3593 | 1.374 | 1.3851 | 1.3845 | 1.3885 | 1.3998 | 1.4186 | 1.4339 | 1.4412 | 1.4439 | 1.4568 | 1.4766 | 1.5012 | 1.5188 | 1.5334 | 1.5432 | 1.5531 | 1.5624 | 1.5744 | 1.5863 | 1.5983 | 1.6103 | 1.6222 | 1.6342 | 1.6461 | 1.6581 | 1.67 | 1.682
Chart: High Price ($100/bbl)
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Mined bitumen | 1.4769 | 1.6071 | 1.6615 | 1.6716 | 1.7028 | 1.747 | 1.7557 | 1.7725 | 1.8054 | 1.8305 | 1.8306 | 1.8306 | 1.8644 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847 | 1.8847
In situ bitumen | 1.6457 | 1.7874 | 1.8611 | 1.9628 | 2.0757 | 2.2692 | 2.4269 | 2.5193 | 2.6679 | 2.7378 | 2.823 | 2.8785 | 2.9827 | 3.0991 | 3.161 | 3.2222 | 3.2681 | 3.2992 | 3.3524 | 3.4165 | 3.4586 | 3.4728 | 3.4808 | 3.5183 | 3.5557 | 3.5932 | 3.6307 | 3.6681 | 3.7056 | 3.743 | 3.7805 | 3.8179 | 3.8554
Conventional oil | 1.2527 | 1.3169 | 1.3574 | 1.4431 | 1.5066 | 1.6347 | 1.7556 | 1.868 | 1.9618 | 2.0592 | 2.1246 | 2.1914 | 2.247 | 2.2975 | 2.3487 | 2.4113 | 2.4555 | 2.5054 | 2.5532 | 2.5907 | 2.6002 | 2.6135 | 2.6169 | 2.6383 | 2.6596 | 2.681 | 2.7024 | 2.7238 | 2.7451 | 2.7665 | 2.7879 | 2.8093 | 2.8306
CER projection to 2040, extrapolated to 2050

## Slide 59: WEAP-CANADA OIL AND GAS SCENARIO RESULTS
Chart: WEAP-Canada water withdrawals, all oil and gas subsectors
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Reference | 572.5657 | 589.9766 | 597.6033 | 601.2241 | 604.771 | 613.6987 | 618.6015 | 618.1235 | 622.9778 | 613.4027 | 619.8165 | 620.4579 | 636.9939 | 641.3327 | 637.2827 | 638.852 | 641.1354 | 642.6713 | 644.785 | 645.7249 | 648.185 | 650.4262 | 652.6597 | 654.666 | 656.621 | 658.6366 | 660.5949 | 662.6116 | 664.523 | 666.5992 | 668.7741 | 671.0483 | 673.2784
Low price | 574.0493 | 572.6039 | 574.3789 | 572.1666 | 571.9904 | 579.0544 | 582.22 | 576.6255 | 577.5914 | 564.8126 | 567.6494 | 564.4322 | 575.3693 | 572.8427 | 562.1447 | 557.9125 | 556.2274 | 552.1848 | 548.3004 | 544.8572 | 542.7614 | 540.2976 | 537.9461 | 535.2091 | 532.3676 | 529.6405 | 526.9088 | 524.1858 | 521.3605 | 518.6997 | 515.8841 | 513.1193 | 510.4166
High price | 574.052 | 594.036 | 606.6946 | 614.7175 | 626.6364 | 651.0271 | 662.1418 | 666.9162 | 682.995 | 680.2958 | 689.1078 | 691.0302 | 715.2618 | 725.0983 | 722.3218 | 725.893 | 730.2167 | 733.4126 | 737.9796 | 740.9441 | 743.8084 | 746.4049 | 748.569 | 751.5263 | 754.5363 | 757.4929 | 760.444 | 763.3465 | 766.2937 | 769.2979 | 772.2449 | 775.2445 | 778.1876
+36%
+18%
-11%
2018: 0%
CER reference, low, or high price projections for activity levels
No assumed footprint (water intensity) improvements

## Slide 60: WEAP-CANADA OIL AND GAS FUTURE WORK
Additional scenarios to be created for:
  Process improvements
  Technology advancement
  Regulatory policies
Integration of LEAP and WEAP

## Slide 61: GENERALIZED MODELLING APPROACH
Process Modelling
Environmental Assessment/
Cost Estimation
Energy/Water Modelling
Outputs
Technology characterization
e.g. Renewable-based power generation
Specification of unit operations for each alternative pathways
Characterization process equipment for unit operations
Determination of energy/resource inputs for each process equipment
Environmental Modelling
(Life Cycle Assessment)
g CO2 eq per unit output
m3 water per unit output
Economic Modelling
(Techno-Economic Assessment)
Cost metrics
$ per unit output
Water modelling
(WEAP - Water Evaluation And Planning)
Canada-wide
Water demand
Water supply
Energy modelling
(LEAP - Long-range Energy Alternatives Planning)
Canada-wide
Energy demand
Energy supply
Long-term annual results per scenario
Total water withdrawal
Total water consumption
Total water savings
Long-term annual results per scenario
Energy demand
Technology use
GHG emissions
System costs
$/tonne of CO2 abatement
$/liter of water saved

## Slide 62: LEAP-WEAP INTEGRATION
INTEGRATED ASSESSMENT OF ENVIRONMENTAL FOOTPRINTS FOR ENERGY PATHWAYS

## Slide 63: INTEGRATED ASSESSMENT OF ENVIRONMENTAL FOOTPRINTS OF ENERGY PATHWAYS - WHY?
Why do integrated assessments?
  Energy transition will have multifaceted impacts
  Energy transition involves systems
What energy pathways?
  GHG reduction measures
    Sector structure change
    Energy efficiency
    Technology change
    Energy and environmental policy
What environmental footprints?
  GHG emissions
  Energy use
  Freshwater use
  System costs  marginal GHG abatement cost
Energy pathways
Technology change
Impacts to water use?
System GHG reductions
System cost impacts

## Slide 65: BACKGROUND – ELECTRICITY SECTOR
Electricity generation sector~ 11% of Canada’s GHG emissions
Thermal power ~ 70% water withdrawal, 11% of water consumption
Major transition underway - the impacts on water resources are unknown.
Chart: Millions m3
| Thermal power | Manufacturing | Households | Commercial | Agriculture | Mining | Oil and gas
Water withdrawal | 25635 | 3954 | 3239 | 2074 | 2007 | 976 | 402
Water consumption | 397 | 411 | 324 | 207 | 1600 | 300 | 382
Chart: 
| Oil and gas | Transportation | Buildings | Electricity | Heavy industry | Agriculture | Waste and others
 | 195 | 174 | 85 | 74 | 73 | 72 | 42
Canada’s GHG emissions by sectors in 2017
[Environment and Climate Change Canada, 2019]
Canada’s water withdrawal and consumption by sectors in 2013
[Environment and Climate Change Canada, 2016]

## Slide 66: LEAP-CANADA ELECTRICITY GENERATION MODEL
Canada’s electricity sector
  Sector transition
    Annual capacity building to meet sub-annual demand
Some plants reaching end of life
Electricity demands grow
Electricity required
(Domestic demand + exports – imports)
This year
(2020)
2050
Next year
(2021)
…
…
…
Generation
capacity

## Slide 67: LEAP-CANADA ELECTRICITY GENERATION MODEL
Canada’s electricity sector
  Sector transition
    Annual capacity building to meet sub-annual demand
Some plants reaching end of life
Electricity demands grow
Electricity required
(Domestic demand + exports – imports)
This year
(2020)
2050
Next year
(2021)
…
…
…
Generation
capacity
Sub-annual
time slices

## Slide 68: LEAP-CANADA ELECTRICITY GENERATION MODEL
Canada’s electricity sector
  Sector transition
    Annual capacity building to meet sub-annual demand
Some plants reaching end of life
Electricity demands grow
Electricity required
(Domestic demand + exports – imports)
This year
(2020)
2050
Next year
(2021)
…
…
…
New capacity needs to be added
Choose mix of technologies that will:
Meet policy targets
Have available resources
Provide min. firm reserve margin at peak demand
Produce the lowest system NPV
Reserve margin
Generation
capacity

## Slide 69: LEAP-CANADA ELECTRICITY GENERATION MODEL
Canada’s electricity sector
  Sector transition
    Annual capacity building to meet sub-annual demand
Electricity required
This year
(2020)
2050
Next year
(2021)
…
…
…
Generation
capacity
Generation
capacity

## Slide 70: LEAP-CANADA ELECTRICITY GENERATION MODEL
Canada’s electricity sector
  Sector transition
    Annual capacity building to meet sub-annual demand
Electricity required
This year
(2020)
2050
Next year
(2021)
…
…
…
Generation
capacity
Generation
capacity

## Slide 71: LEAP-CANADA ELECTRICITY GENERATION MODEL
Canada’s electricity sector
  Sector transition
    Annual capacity building to meet sub-annual demand
Electricity required
This year
(2020)
2050
Next year
(2021)
…
…
…
Generation
capacity
Generation
capacity
Dispatch based on:
-Operating cost (ղ, carbon price policy, fuel prices)
-Policy targets (Regional renewable generation requirements, carbon reduction requirements)

## Slide 72: LEAP-CANADA ELECTRICITY GENERATION MODEL
Canada’s electricity sector
  Sector transition
    Annual capacity building to meet sub-annual demand
Electricity required
This year
(2020)
2050
Next year
(2021)
…
…
…
Generation
capacity
Link GWh of generation data to WEAP-Canada
Generation
capacity
Key results:
GHG emissions
System costs
Electricity generation by technology

## Slide 73
Unique for each scenario

## Slide 74: WEAP-CANADA ELECTRICITY MODEL

## Slide 75: WEAP-CANADA ELECTRICITY MODEL

## Slide 76
Annual activity level for demand site

## Slide 78
Annual activity level for demand site
MWhs of generation from LEAP
Share of generation from watershed

## Slide 80
Life cycle water footprints

## Slide 81: WEAP-CANADA ELECTRICITY MODEL

## Slide 82: GENERALIZED MODELLING APPROACH
Process Modelling
Environmental Assessment/
Cost Estimation
Energy/Water Modelling
Outputs
Technology characterization
e.g. Renewable-based power generation
Specification of unit operations for each alternative pathways
Characterization process equipment for unit operations
Determination of energy/resource inputs for each process equipment
Environmental Modelling
(Life Cycle Assessment)
g CO2 eq per unit output
m3 water per unit output
Economic Modelling
(Techno-Economic Assessment)
Cost metrics
$ per unit output
Water modelling
(WEAP - Water Evaluation And Planning)
Canada-wide
Water demand
Water supply
Energy modelling
(LEAP - Long-range Energy Alternatives Planning)
Canada-wide
Energy demand
Energy supply
Long-term annual results per scenario
Total water withdrawal
Total water consumption
Total water savings
Long-term annual results per scenario
Energy demand
Technology use
GHG emissions
System costs
$/tonne of CO2 abatement
$/liter of water saved

## Slide 83: INTEGRATING RESULTS: WATER-GHG PROJECTION
Chart: Water consumption in millions m3
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Curr_pol_water_consump | 4826312704.9384 | 4759602571.1841 | 4848836852.3355 | 4888858940.0927 | 4902429798.8568 | 4880040933.0786 | 5089438767.468 | 5108770464.0779 | 5138235308.9588 | 5217455207.5438 | 5308149966.1366 | 5327143351.1924 | 5448312883.7735 | 5453442538.3213 | 5441621822.1641 | 5410917476.9655 | 5432874147.3581 | 5427982659.2773 | 5421584002.8907 | 5430768833.6739 | 5550415804.7136 | 5574022221.8755 | 5580296169.0687 | 5580678523.763 | 5575395513.2753 | 5592129394.8302 | 5594530689.7051 | 5579654810.7069 | 5594193169.6052 | 5595565082.5418 | 5599835834.2952 | 5589080917.7222 | 5577494508.6448 | 5573192000.4947 | 5555359030.6316 | 5531956686.2669 | 5529027683.2335 | 5546989500.6274 | 5547314870.9985 | 5547248136.3716 | 5552114586.5202 | 5551419846.2051 | 5547471126.5984 | 5545155051.308 | 5564191460.1322 | 5578313978.4661
Curr_pol_emissions | 109375.6591 | 106703.6552 | 108239.1335 | 113768.1666 | 86989.5286 | 89345.1492 | 87631.1348 | 87817.1519 | 86389.4105 | 83282.0051 | 80857.5236 | 80324.4615 | 82133.0468 | 80723.2738 | 80265.2792 | 58961.9988 | 52467.1886 | 49635.9953 | 49208.7567 | 48806.0005 | 49074.8408 | 47017.8394 | 46549.8823 | 42858.5307 | 42515.0328 | 40345.9745 | 40138.487 | 39721.658 | 39125.4519 | 38622.3084 | 38065.8046 | 37298.3247 | 34778.9395 | 33981.0795 | 32664.8692 | 31916.3814 | 31023.8365 | 27879.3586 | 27557.8279 | 27141.0256 | 26950.2826 | 27029.729 | 26940.0121 | 26958.5001 | 26895.1695 | 27012.1459
Future
Historical
Water consumption
from WEAP
GHG emissions from LEAP
Example - least cost electricity system scenario results

## Slide 84: INTEGRATING RESULTS: WATER-GHG CHANGE FOR SCENARIO
Chart: Water consumption (millions m3)
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Bottom | 4826312704.9384 | 4759602571.1841 | 4848836852.3355 | 4888858940.0927 | 4902429798.8568 | 4880040933.0786 | 5089438767.468 | 5108770464.0779 | 5138235308.9588 | 5217455207.5438 | 5308149966.1366 | 5327143351.1924 | 5448312883.7735 | 5453442538.3213 | 5441621822.1641 | 5410917476.9655 | 5432874147.3581 | 5427982659.2773 | 5421584002.8907 | 5430768833.6739 | 5550415804.7136 | 5574022221.8755 | 5580296169.0687 | 5580678523.763 | 5575395513.2753 | 5592129394.8302 | 5594530689.7051 | 5579654810.7069 | 5594193169.6052 | 5595565082.5418 | 5599835834.2952 | 5589080917.7222 | 5577494508.6448 | 5573192000.4947 | 5555359030.6316 | 5531956686.2669 | 5529027683.2335 | 5546989500.6274 | 5547314870.9985 | 5547248136.3716 | 5552114586.5202 | 5551419846.2051 | 5547471126.5984 | 5545155051.308 | 5564191460.1322 | 5578313978.4661
Gap | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1419808.1243 | 3652279.4905 | 3829202.0309 | -819026.4667 | -1667616.4387 | -1395696.479 | -1478095.831 | -490579.757 | 7798471.9466 | 15635099.4132 | 146940589.0625 | 147025447.7088 | 145917141.8038 | 152759955.6324 | 224039806.3384 | 259032274.2448 | 297482983.8353 | 333599475.5334 | 400055805.5023 | 415044794.4721 | 456346084.507 | 467770788.6775 | 481331017.2138 | 511472082.7482 | 543984971.1001 | 602751798.4788 | 658637079.8354 | 636517163.8152 | 675043450.7367 | 715239591.0221 | 722057958.0703
Bottom | 109375.6591 | 106703.6552 | 108239.1335 | 113768.1666 | 86989.5286 | 89345.1492 | 87631.1348 | 87817.1519 | 86389.4105 | 83282.0051 | 80857.5236 | 80324.4615 | 82133.0468 | 80723.2738 | 80265.2792 | 59273.6285 | 52738.8947 | 50012.8856 | 49777.5763 | 49432.1331 | 49752.2195 | 47580.3292 | 47167.7603 | 44323.4703 | 43979.7626 | 33773.2526 | 33348.2968 | 32650.7743 | 31847.3097 | 30049.4246 | 28225.9987 | 26403.4171 | 24557.841 | 22774.5155 | 20947.8166 | 18059.6859 | 17038.0508 | 14893.8094 | 13143.2733 | 11326.7532 | 9174.2379 | 8174.2379 | 6174.2379 | 4174.2379 | 2174.2379 | 500
Gap | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | -311.6297 | -271.7061 | -376.8903 | -568.8196 | -626.1326 | -677.3787 | -562.4898 | -617.878 | -1464.9396 | -1464.7298 | 6572.7219 | 6790.1902 | 7070.8837 | 7278.1422 | 8572.8838 | 9839.8059 | 10894.9076 | 10221.0984 | 11206.564 | 11717.0526 | 13856.6956 | 13985.7857 | 12985.5492 | 14414.5545 | 15814.2724 | 17776.0447 | 18855.491 | 20765.7742 | 22784.2621 | 24720.9315 | 26512.1459
Decarb_water_consump | 4826312704.9384 | 4759602571.1841 | 4848836852.3355 | 4888858940.0927 | 4902429798.8568 | 4880040933.0786 | 5089438767.468 | 5108770464.0779 | 5138235308.9588 | 5217455207.5438 | 5308149966.1366 | 5327143351.1924 | 5448312883.7735 | 5453442538.3213 | 5441621822.1641 | 5412337285.0898 | 5436526426.8485 | 5431811861.3082 | 5420764976.424 | 5429101217.2352 | 5549020108.2346 | 5572544126.0445 | 5579805589.3118 | 5588476995.7097 | 5591030612.6886 | 5739069983.8926 | 5741556137.4139 | 5725571952.5107 | 5746953125.2376 | 5819604888.8802 | 5858868108.5401 | 5886563901.5575 | 5911093984.1782 | 5973247805.997 | 5970403825.1037 | 5988302770.7739 | 5996798471.911 | 6028320517.8413 | 6058786953.7467 | 6091233107.4717 | 6154866384.999 | 6210056926.0405 | 6183988290.4136 | 6220198502.0447 | 6279431051.1543 | 6300371936.5365
Curr_pol_water_consump | 4826312704.9384 | 4759602571.1841 | 4848836852.3355 | 4888858940.0927 | 4902429798.8568 | 4880040933.0786 | 5089438767.468 | 5108770464.0779 | 5138235308.9588 | 5217455207.5438 | 5308149966.1366 | 5327143351.1924 | 5448312883.7735 | 5453442538.3213 | 5441621822.1641 | 5410917476.9655 | 5432874147.3581 | 5427982659.2773 | 5421584002.8907 | 5430768833.6739 | 5550415804.7136 | 5574022221.8755 | 5580296169.0687 | 5580678523.763 | 5575395513.2753 | 5592129394.8302 | 5594530689.7051 | 5579654810.7069 | 5594193169.6052 | 5595565082.5418 | 5599835834.2952 | 5589080917.7222 | 5577494508.6448 | 5573192000.4947 | 5555359030.6316 | 5531956686.2669 | 5529027683.2335 | 5546989500.6274 | 5547314870.9985 | 5547248136.3716 | 5552114586.5202 | 5551419846.2051 | 5547471126.5984 | 5545155051.308 | 5564191460.1322 | 5578313978.4661
Curr_pol_emissions | 109375.6591 | 106703.6552 | 108239.1335 | 113768.1666 | 86989.5286 | 89345.1492 | 87631.1348 | 87817.1519 | 86389.4105 | 83282.0051 | 80857.5236 | 80324.4615 | 82133.0468 | 80723.2738 | 80265.2792 | 58961.9988 | 52467.1886 | 49635.9953 | 49208.7567 | 48806.0005 | 49074.8408 | 47017.8394 | 46549.8823 | 42858.5307 | 42515.0328 | 40345.9745 | 40138.487 | 39721.658 | 39125.4519 | 38622.3084 | 38065.8046 | 37298.3247 | 34778.9395 | 33981.0795 | 32664.8692 | 31916.3814 | 31023.8365 | 27879.3586 | 27557.8279 | 27141.0256 | 26950.2826 | 27029.729 | 26940.0121 | 26958.5001 | 26895.1695 | 27012.1459
Decarb_emissions | 109375.6591 | 106703.6552 | 108239.1335 | 113768.1666 | 86989.5286 | 89345.1492 | 87631.1348 | 87817.1519 | 86389.4105 | 83282.0051 | 80857.5236 | 80324.4615 | 82133.0468 | 80723.2738 | 80265.2792 | 59273.6285 | 52738.8947 | 50012.8856 | 49777.5763 | 49432.1331 | 49752.2195 | 47580.3292 | 47167.7603 | 44323.4703 | 43979.7626 | 33773.2526 | 33348.2968 | 32650.7743 | 31847.3097 | 30049.4246 | 28225.9987 | 26403.4171 | 24557.841 | 22774.5155 | 20947.8166 | 18059.6859 | 17038.0508 | 14893.8094 | 13143.2733 | 11326.7532 | 9174.2379 | 8174.2379 | 6174.2379 | 4174.2379 | 2174.2379 | 500
Future
Historical
Baseline water consumption
(blue line)
Baseline GHG emissions (blackline)
Change due to decarbonization scenario

## Slide 85: INTEGRATING RESULTS: WATER-GHG-COST BUBBLE CHART
Example - Water-GHG-cost tradeoffs for decarbonization scenario compared to baseline
(2020-2050)

## Slide 87: LEAP-WEAP-CANADA FUTURE WORK
Additional scenarios to be created for:
Process improvements
  Technology advancement
  Regulatory policies
Integration of LEAP and WEAP

## Slide 88: LIST OF OUR RESEARCH WITH LEAP & WEAP

## Slide 89: PUBLICATIONS, IN-REVIEW PAPERS 1/2
GHG mitigation assessments:
Subramanyam V, Kumar A, Talaei A, Mondal MAH. Energy efficiency improvement opportunities and associated greenhouse gas abatement costs for the residential sector, Energy, 2017, 118: 795-807.
Subramanyam V, Ahiduzzaman M, Kumar A. Greenhouse gas emissions mitigation potential in the commercial and institutional sector, Energy and Buildings, 2017, 140: 295-304.
Bonyad M, Shafique HU, Mondal MAH, Subramanyam V, Kumar A, Ahiduzzaman M. Development of a framework for the assessment of energy demand-based greenhouse gas mitigation options for the agriculture sector, Transactions of the ASABE, 2018, 61:763.
Talaei A, Ahiduzzaman M, Kumar A. Assessment of Long-term energy efficiency improvement and greenhouse gas emissions mitigation potentials in the chemical sector, Energy, 2018; 153: 231-47.
Talaei A, Pier D, Iyer AV, Ahiduzzaman M, Kumar A. Assessment of long-term energy efficiency improvement and greenhouse gas emissions mitigation options for the cement industry, Energy, 2019, 170:1051-1066.
Katta AK, Davis M, Subramanyam V, Dar AF, Mondal MAH, Ahiduzzaman M, Kumar A. Assessment of energy demand-based greenhouse gas mitigation options for Canada’s oil sands, Journal of Cleaner Production, 2019, 241: 118306.
Talaei A, Oni O, Ahiduzzaman M, Roychaudhuri PS, Rutherford J, Kumar A. Assessment of the impacts of process-level energy efficiency improvement on the greenhouse gas mitigation potential in the petroleum refining sector, Energy, In Press, 2019.
Talaei A, Ahiduzzaman M, Kumar A. Potential for energy efficiency improvement and greenhouse gas mitigation from Canada’s iron and steel industry, 2019. (in review)
Katta A, Davis M, and Kumar A, Assessment of greenhouse gas mitigation options for the iron, gold, and potash mining sectors, Journal of Cleaner Production, vol. 245, p. 118718, 2020.
Janzen R, Davis M, and Kumar A, Greenhouse gas emission abatement potential and associated costs of integrating renewable and low carbon energy technologies into the Canadian oil sands., Submitted., 2019.
Janzen R, Davis M, and Kumar A, An assessment of opportunities for cogenerating electricity to reduce greenhouse gas emissions in the oil sands., Submitted., 2020.
Janzen R, Davis M, and Kumar A, Evaluating long-term greenhouse gas mitigation opportunities through carbon capture, utilization, and storage in the oil sands., Submitted., 2020.
Davis M, Moronkeji A, Ahiduzzaman M, and Kumar A, The development of an energy-environment model for assessing renewable generation pathways for a fossil fuel-based electricity-producing jurisdiction, Submitted, 2020.

## Slide 90: PUBLICATIONS, IN-REVIEW PAPERS 2/2
Energy assessments:
Subramanyam V, Paramshivan D, Kumar A, Mondal MAH. Using Sankey diagrams to map energy flow from primary fuel to end use, Energy Conversion and Management, 2015, 91: 342-52.
Davis M, Ahiduzzaman M, Kumar A. How will Canada’s greenhouse gas emissions change by 2050? A disaggregated analysis of past and future greenhouse gas emissions using bottom-up energy modelling and Sankey diagrams, Applied Energy, 2018, 220: 754-86.
Davis M, Ahiduzzaman M, Kumar A. Mapping Canadian energy flow from primary fuel to end use, Energy Conversion and Management, 2018, 156: 178-91.
Davis M, Ahiduzzaman M, Kumar A. How to model a complex national energy system? Developing an integrated energy systems framework for long-term energy and emissions analysis, International Journal of Global Warming, 2019, Vol. 17, No. 1.
Katta AK, Davis M, and Kumar A, Development of disaggregated energy use and greenhouse gas emission footprints in Canada’s iron, gold, and potash mining sectors, Resources, Conservation and Recycling, vol. 152, p. 104485, 2020.
Life cycle water assessments:
Ali B, and Kumar A, Development of life cycle water-demand coefficients for coal-based power generation technologies, Energy Conversion and Management, vol. 90, pp. 247-260, 2015.
Ali B, and Kumar A, Development of life cycle water footprints for gas-fired power generation technologies, Energy Conversion and Management, vol. 110, pp. 386-396, 2016.
Ali B, and Kumar A, Development of water demand coefficients for power generation from renewable energy technologies, Energy Conversion and Management, vol. 143, pp. 470-481, 2017.
Ali B, and Kumar A, Development of life cycle water footprints for oil sands-based transportation fuel production, Energy, vol. 131, pp. 41-49, 2017.
Ali B, and Kumar A, Life cycle water demand coefficients for crude oil production from five North American locations, Water Research, vol. 123, pp. 290-300, 2017.
Integrated assessments:
Agrawal N, Ahiduzzaman M, and Kumar A, The development of an integrated model for the assessment of water and GHG footprints for the power generation sector, Applied Energy, vol. 216, pp. 558-575, 2018.

## Slide 91: CURRENT WORK
GHG mitigation assessments:
Shafique U, Davis M, Owttrim C, Paul P, Ahiduzzaman A, Kumar A. Development of a framework for the Assessment of Energy Demand based GHG Mitigation Options for the Alberta Pulp and Paper Sector.
Haider M, Davis M, Subramanyam V, Kumar A, Radpour S, Mondal A, Ahiduzzaman A. Assessment of Greenhouse Gas Mitigation Options for the Transportation Sector using the LEAP Model.
Energy assessments:
Owttrim C, Davis M, Kumar A. Development of long-term energy efficiency potential in the pulp and paper sector.
Radpour S, Owttrim C, Davis M, Talaei A, Kumar A. Development of long-term energy efficiency potential in the iron and steel sector.
Water assessments:
Agrawal N, Patrick T, Davis M, Gemechu E, Ahiduzzaman A, Kumar A. Mapping water flows in Canada with Sankey diagrams.
Patrick T, Gupta A, Davis M, Kumar A. Development of an oil and gas water evaluation and planning model.

## Slide 92: ACKNOWLEDGMENTS
Thanks to the NSERC/Cenovus/Alberta Innovates Associate Industrial Research Chair in Energy and Environmental Systems Engineering and the Cenovus Energy Endowed Chair in Environmental Engineering for providing financial support.
We are also grateful to representatives from Alberta Innovates, Suncor Energy Inc., Cenovus Energy Inc., Natural Resources Canada, and Environment and Climate Change Canada for their valuable inputs and comments in various forms.
As a part of the University of Alberta's Future Energy Systems (FES) research initiative, this research was made possible in part thanks to funding from the Canada First Research Excellence Fund (CFREF).